## Slide 1: TraceRoute
Sean Aryana, Andrew Gammon, Keith yang
cse481L – Spring 2015

## Slide 2: Motivation
Interior navigation. Orient yourself without using GPS! (Pedestrian dead reckoning)
Saves power, and can give you movement data in 3D space
Phones have lots of cool sensors to play with
It’s a field of active research and experimentation!
Has many possible use cases (i.e. museums, aquarium)

## Slide 3: What we Learned - Sensors
Accelerometer produces incredibly noisy data
Gyroscope tends to drift as time goes on
Compass needs to be oriented on a flat surface
Barometer measurements bounce around
Step detector can be delayed

## Slide 4: What we Learned - Navigation
Distance
  Double integrating acceleration would produce too much error
  Stride length from height and gender of the user decent indicator
Direction
  Accelerometer too sporadic for accurate direction
  Gyroscope doesn’t indicate which way user is moving
  Compass does a decent job
Altitude
  Barometer will level out over time

## Slide 5: So how did we get things to work?
Sensor Fusion!
  Detect drift and then set up new standard
  Use multiple sources for direction
Low pass filters makes the sensors data less noisy

## Slide 6: What we Learned - OpenGL
Lots of math!
Clumsy API – OpenGL ES
Things that are intuitive from a user perspective (camera control, lighting) are fairly involved processes

## Slide 7: What we Built
Main Screen
User Settings
VR Mode
Path Manager

## Slide 9: Where to go from here?
Bluetooth beacons or other access points
  Better direction detection
  Accurate positioning
Push cards to phone based off of position
Kalman filter for path prediction

## Slide 10: Want to learn more?
Sean Aryana (saryana0@uw.edu)
Andrew Gammon (gammoa@uw.edu)
Keith Yang (keith619@cs.washington.edu)
GitHub: https://github.com/saryana/TraceRoute
Detailed video: https://www.youtube.com/watch?v=4LEQh_zvMzM&feature=youtu.be